## Slide 1
CAPSTONE · AIR TRAFFIC SURVEILLANCE
Business Problem Statement
LOCKHEED MARTIN PROPRIETARY INFORMATION
Thomas Rathbun, PhD · LOCKHEED MARTIN PROPRIETARY INFORMATION
Air traffic surveillance still depends on a fragmented pipeline: each radar runs its own tracker, then a separate correlator tries to resolve duplicates across sensors. That design is costly to maintain, slow to adapt to clutter and sensor bias, and hard to scale as airspace density and multi-radar coverage grow.
01
Operational Complexity
Per-sensor physics trackers plus a downstream correlator create many failure points, hand-tuned gates, and high sustainment cost.
02
Fusion Ambiguity
PSR clutter, SSR intermittency, registration bias, and asynchronous scans produce duplicate tracks and ID switches.
03
Limited Adaptivity
Rule-based association does not learn from data and struggles with non-linear maneuvers and novel clutter without expert re-tuning.
Opportunity: Evaluate a unified AI/ML tracker-correlator that simplifies the stack while meeting operational tracking quality.
1 / 7

## Slide 2
CAPSTONE · AIR TRAFFIC SURVEILLANCE
Proposed Solution
LOCKHEED MARTIN PROPRIETARY INFORMATION
Thomas Rathbun, PhD · LOCKHEED MARTIN PROPRIETARY INFORMATION
A hybrid AI/ML tracker-correlator that ingests multi-sensor radar plots (PSR/SSR), learns association and clutter rejection, and produces a single correlated track picture—keeping physics-based state estimation where it is strongest.
1
Clutter Filter
Unary MLP scores false alarms early to cut noise before association.
2
Learned Association
Dual pairwise classifiers (PSR kinematics + SSR identity) fuse multi-sensor reports.
3
Async Kalman Update
Exact-time prediction/update removes temporal dragging across staggered scans.
4
Track Management
M/N initiation, coasting, and de-duplicated correlated outputs.
Research path: pairwise + hybrid baseline → assess pure GNN/transformer correlator feasibility → document recommendations for production path.
2 / 7

## Slide 3
CAPSTONE · AIR TRAFFIC SURVEILLANCE
ROI Calculation / Value Statement
LOCKHEED MARTIN PROPRIETARY INFORMATION
Thomas Rathbun, PhD · LOCKHEED MARTIN PROPRIETARY INFORMATION
This is a feasibility capstone: value is measured in reduced system complexity, tracking quality, and a clear go / no-go path—not immediate product revenue.
Engineering Efficiency
Fewer hand-tuned association gates per sensor suite
One fused pipeline vs. N trackers + correlator
Reusable evaluation harness (MOTA, ID switches)
Operational Quality
Target: high MOTA / precision with near-zero ID switches on sim streams
Better multi-radar de-duplication → cleaner common operating picture
Earlier clutter rejection → lower downstream load
Strategic Upside
Evidence package for ML investment vs. pure classical fusion
Identifies where hybrid beats end-to-end deep models
De-risks future transformer / GNN correlator work
3 / 7

## Slide 4
CAPSTONE · AIR TRAFFIC SURVEILLANCE
End-user Stakeholder(s) and Roles
LOCKHEED MARTIN PROPRIETARY INFORMATION
Thomas Rathbun, PhD · LOCKHEED MARTIN PROPRIETARY INFORMATION
Stakeholder
Interest / Need
Role in Capstone
Surveillance / ATC Engineering
Primary consumers of architecture, metrics, and integration guidance for multi-radar fusion.
Review design; assess fit vs. current correlators.
Tracker / Sensor Fusion SMEs
Validate association, clutter, and async-timing assumptions against operational practice.
Technical review of hybrid vs. pure-ML results.
Data / ML Engineering
Own training data pipelines, labeling, and model ops if the approach is adopted.
Advise on data quality, schema, and retrain path.
Product / Program Leadership
Decide investment: extend hybrid, pursue transformer correlator, or stay classical.
Use feasibility + risk findings for roadmap.
Operations (future users)
Need a stable common track picture with low false tracks and ID stability.
Indirect; success criteria framed around their COP quality.
4 / 7

## Slide 5
CAPSTONE · AIR TRAFFIC SURVEILLANCE
Data Requirements
LOCKHEED MARTIN PROPRIETARY INFORMATION
Thomas Rathbun, PhD · LOCKHEED MARTIN PROPRIETARY INFORMATION
Inputs
Multi-sensor plots: PSR position/velocity/amplitude; SSR Mode 3A/S + position
Decoded Asterix-style streams (CAT 048 / 062 derived) in Cartesian form
Timestamps, sensor IDs, and modality tags for async fusion
Labels / Truth
Ground-truth track IDs for association training & MOTA
True kinematics (x,y,z,vx,vy,vz) independent of noisy plots
Clutter / false-alarm flags where available
Quality Bars
Canonical schema (one field language across sim & real)
Scenario splits by track / time / region (no leakage)
Hard negatives: crossing tracks, multi-radar bias, dropouts
Current project assets
Synthetic multi-radar JSONL streams · CAT-62–derived scenarios · Pairwise/clutter training sets · Eval metrics (MOTA, MOTP, ID switches). Gap: clean regional real-data packages and consistent GT kinematics remain a risk for pure end-to-end models.
5 / 7

## Slide 6
CAPSTONE · AIR TRAFFIC SURVEILLANCE
Deliverable and Due Date
LOCKHEED MARTIN PROPRIETARY INFORMATION
Thomas Rathbun, PhD · LOCKHEED MARTIN PROPRIETARY INFORMATION
Hard constraint
Write-up due 2 Sep 2026 · Leave starts 20 Aug 2026 → all substantive work, demos, and draft write-up complete by 19 Aug 2026.
1
Technical write-up
Problem, method, experiments, results, recommendations
2 Sep (draft 19 Aug)
2
Working prototype
Hybrid + pairwise pipeline; selected model experiments
≤ 15 Aug
3
Evaluation package
Metrics tables, plots/GIFs, baseline comparison
≤ 18 Aug
4
Stakeholder brief
This deck + short demo narrative
≤ 19 Aug
6 / 7

## Slide 7
CAPSTONE · AIR TRAFFIC SURVEILLANCE
Risks / Issues
LOCKHEED MARTIN PROPRIETARY INFORMATION
Thomas Rathbun, PhD · LOCKHEED MARTIN PROPRIETARY INFORMATION
HIGH
Schedule compression (leave 20 Aug)
Official due date is 2 Sep, but availability ends 19 Aug. Mitigation: freeze scope now; finalize draft + metrics before leave; buffer only for light edits if reachable remotely.
HIGH
Data quality & label noise
Schema inconsistency, reconstructed GT, and region mislabels hurt pure end-to-end models. Mitigation: prioritize hybrid baseline; document data gaps honestly; fix only highest-impact QA items.
MED
End-to-end GNN underperformance
Pure GAT models lag hybrid on async streams. Mitigation: treat as research finding, not failure; recommend transformer association + KF path as future work.
MED
Scope creep (new architectures)
Full transformer rebuild may not fit pre-leave window. Mitigation: architecture proposal + limited prototype only if hybrid write-up is locked first.
LOW
Stakeholder access / review lag
Late SME feedback can slip narrative polish. Mitigation: share draft outline mid-July; book one review before 15 Aug.
7 / 7